12/14/10

CONGRATULATIONS

12/14/10

Thank you for purchasing your Table-Tyer Strapping Machine. The Table-Tyer has been designed to be a reliable, maintenance free strapping machine. The innovative design of this machine allows for every maintenance part to be replaced easily and quickly with very little or no instruction.

Considerable effort has been made to ensure that this product conforms to our high quality standards. However, should you experience any difficulties, please contact your Signode Representative with your machine model and serial number.

Thank you for your help.

TABLE-TYER STRAPPING MACHINE PART NO. 500998

All conditions and options have been detailed in this manual to guide and alert operating and service personnel with respect to safety, operation and maintenance procedures. A complete parts listing, with exploded views, has been included in this manual in the event replacement parts must be ordered. Please review each section of

this manual before operating your machine.

PLEASE NOTE: Most of the fasteners in this machine are metric. Before removing and replacing any part, refer to the parts listing to determine the proper tools to use and

the correct size hardware that may have to be replaced.

2

12/14/10

WARNING - READ AND FOLLOW THESE INSTRUCTIONS - FAILURE TO DO THIS COULD RESULT IN SEVERE PERSONAL INJURY.

OPERATING INSTRUCTIONS

1.   Only people trained in the use of strapping machines are to operate or service this machine.

2.   Read all signs on machine. Do not remove, modify or deface any sign. Replace all damaged signs.

3.   Inspect the machine for unsafe conditions - DAILY - and replace all worn or broken parts.

4.   Keep work area uncluttered and well lit.

5.   If you require safety instructions in another language, contact your local Signode representative.

MAINTENANCE

1.   Establish a preventive maintenance program for your machine by following the preventive maintenance program in this manual.

2.   To ensure proper machine operation, use the specified power sources listed in this manual.

3.   Do not overload the machine by exceeding the package size specification.

4.   Remove all packages from the machine before performing service.

5.   Unless otherwise noted in this manual, disconnect and lockout all power before servicing your machine.

6.   Follow all maintenance and service instructions in this manual.

MOVING MACHINE PARTS

1.   Disconnect and lock out all power to Signode's machines before entering the strap chute area.

2.   Never put any part of your body into the strap chute area or machine enclosure with machine power on.

3.   Never stand on the machine table-top.

MACHINE INSTALLATION

1.   All customer interlocks must be connected as shown in this manual's electrical drawings.

Failure to properly connect interlocks can result in improper machine operation and/or personal injury.

2.   Be familiar with the locations of safety interlocks/guards and Emergency Stop Devices - refer to machine manual topic "Disconnect & Lockout Procedures".

3.   Do not defeat any safety interlock or safety device. Do not operate machine with any safety devices/guards removed.

4.   Before operating the machine, ensure that all safety interlocks and Emergency Stop buttons are operating properly.

5.   Unauthorized modifications can present a safety hazard to machine personnel and will void the machine warranty.

6.   Secure the machine in place using the locking casters.

3

12/14/10

PERSONAL PROTECTION

1.   To prevent back or other body injuries, your employer must provide proper lifting and/or handling instructions. Your employer may also contact the National Safety Council, Itasca, IL

60143-0558 for information on lifting techniques.

2.   When removing tensioned strap from a package, proceed as follows:

a.   Wear eye, face and hand protection

b.   Before cutting strap, make sure all personnel are at a safe distance. c.   Hold the strap against the load above the cutter as shown.

d.   Using the proper Signode strap cutter, cut strap as pictured. e.   Stand clear of unheld strap end which will spring out if under

pressure.

3.   Always wear steel reinforced safety shoes.

4.   Always wear safety glasses with side shields which conform to ANSI Standard Z-87.1 or EN 166

5.   Wear protective gloves when handling strap.

ENVIRONMENTAL INFORMATION

The emissions produced during the heat sealing process may be an irritant to some people. Use this machine in areas that are externally ventilated. Should you be affected by these fumes, move away from machine to fresh air.

LOCKOUT/TAGOUT

1.   Follow OSHA 1910.147 (Lockout/Tagout Regulation) for machine lockout procedures and other important lockout/tagout guidelines.

2.   Be familiar with all lockout sources on this machine, refer to the "Lockout & Tagout" section of this manual.

3.   Even after a machine has been locked out, there may be stored energy in the system. To ensure that all stored energy is relieved, wait at least one minute before servicing electrical capacitors and wait 5 minutes for hot knife to cool.

4.   Before performing service in the strap chute area, disconnect and lockout machine power.

MOVING THE MACHINE

Wheel kits are standard for Signode general purpose machines. A forklift may be used to transport the machine from one location to another. Consult your employer for proper lifting and handling methods.

4

12/14/10

TABLE-TYER, MACHINE SPECIFICATIONS

STRAP SIZES:	Signode Empax 1/4" (6mm), 3/8" (9mm), 1/2" (12mm)

PACKAGE SIZE (Minimum):	3 1/2" W x 1-1/2" H

| VOLTAGE SPECIFICATIONS: | Rated current: | 3A |
| --- | --- | --- |
|  | Rated voltage: | 110V |
|  | Rated frequency: | 6OHz |
|  | Type of current: | AC |

FAULT PROTECTION:	Fused

SYSTEM DISCONNECT:	HP Rated switch

OPERATING HEIGHT:	Minimum 30-3/4", Maximum 37-1/2" WEIGHT:	168 lbs.

NOISE EMISSIONS:	55dB

MACHINE DIMENSIONS:

5

12/14/10

MAJOR COMPONENTS - EXTERNAL

1.   Main switch

2.   Heater lamp, lamp will light on when proper sealing temperature is reached

3.   Potentiometer, strap feed length

4.   Button, strap feed and reset

5.   Potentiometer, strap tension adjustment

6.   Table top, hinge

7.   Strap reel

8.   Caster (2 locking)

9.   Adjustable legs (Table-Tyer)

10. Frame

11. Access Door

6

12/14/10

7

12/14/10

MACHINE DISCONNECT AND LOCK-OUT PROCEDURES

This machine is equipped with shut off devices which satisfy OSHA Regulation 1910.147 (control of hazardous energy sources - lock out/tag out).

Become familiar with the location, and operation of each shutoff device.

Disconnect/Lock-Out all power sources before servicing machine. Never use machine operating controls as a means for locking out power.

ELECTRICAL

The machine is ready to operate when connected to the main power supply and the main switch QS I is switched to ON position. It takes approximately I minute for the heating element to reach its operating temperature.

The machine is switched on and off with the main switch QS 1 located on the machine front operating panel.

P	Turn the main disconnect switch to the OFF position.

P	Locate the appropriate locking hole on the switch, and apply a locking device.

NOTE: Some electrical components in the machine may be electrically charged after the power is shut off. Wait no less than one minute after the power has been disconnected before servicing the panel.

8

12/14/10

ELECTRICAL SCHEMATIC, TABLE TYER

9

10

11

12

12/14/10

MACHINE OPERATION

START-UP AND OPERATING SEQUENCE

1.   Put strap on the strap reel and thread the strap.

2.   Turn main switch QS1 to ON. The heating element reaches the working temperature in approximately 1 minute.

3.   Use potentiometer R3 to adjust the strap length.

4.   Place the strap around the package to be strapped and insert the strap into the strapping head until it stops.

5.   The strapping and welding sequence should complete.

6.   At end of strapping sequence the strap end is fed automatically.

7.   R4 adjusts the strap tension.

THREADING STRAP

1.   Turn reel nut handle (A) left and remove it.

2.   Remove the cover of the reel (B) and install the strap reel.

3.   Make sure that the payoff rotation matches directional arrows when unrolling.

4.   Put the reel cover back on and tighten reel nut handle (A) to the right.

5.   Remove all adhesive strips or other adhesive material.

6.   Unroll about 1.5 m strap and make sure that it is not twisted.

7.   Thread the strap in direction of arrow over (C) to roller (D). Continue to thread strap into rollers (E).

8.   Turn left button SA1 (strap feed) until the length you need.

13

12/14/10

STRAP TENSION

If R4 (strap tension adjustment) is on MAX position make sure that A is turned clockwise until the strap is not sliding between rollers B and C.

Reverse action to achieve lower strap tension.

MAINTENANCE AND LUBRICATION

To ensure that the semi-automatic strapping machine is always ready for proper and reliable operation keep to regular and attentive

maintenance. Keep the machine clean and take care particularly of the strap guides. All small particles of loose strap should always be removed from all parts of the machine. In addition to

the strap guides, the strap feed devices of the unit, the top of the dies and the feed devices on the strap magazine have to be blown free of any dust at least once per week. The dies on the unit have to be lightly lubricated

weekly.

Lubricate the marked points weekly. Use only resin-free brand name oil for lubrication.  All other assemblies are maintenance free. The strap guides and the sealing unit have to be kept clean! Do not oil feedrollers.

14

12/14/10

15

12/14/10

CONTROL HEAD GROUP ASSEMBLY

KEY	QTY	PART NO.	DESCRIPTION

1	1	500475	Main Body Block

2	1	500476	Switch Lever

3	1	500477	Switch Pin

4	1	500478	Strap Guide (A)

5	1	500479	Strap Guide (B)

6	1	500480	Switch Bracket

7	1	500481	Cutter Holder

8	1	500482	Bar Guide Lid

9	1	500483	Spring Hook

10	1	500484	Shaft

11	1	500485	Arm

12	1	500486	Return Spring

13	2	500487	Collar

14	1	500488	Slide

15	1	500489	Separator

16	1	500490	Guide (L)

17	1	500491	Guide (R)

18	1	500492	Gum

19	1	500493	Front Plate

20	1	500494	Guide Front

21	4	500495	HBS, M6x16

22	4	500496	HBS, M5x12

23	1	500497	HBS, M5x25

24	1	500498	Bearing 635ZZ

25	4	500499	PW,M5

26	1	500500	SW,M5

27	2	500501	HN, M5

28	1	500502	PMS, M4x20

29	1	500503	HN,M4

30	1	500504	Spring Pin, 6x20

31	2	500505	HSS, M6x6

32	2	500506	HN,M8

33	1	500507	SW,M8

34	4	500508	SW,M6

35	3	500509	Spring Pin, 3x12

36	1	500510	HBS, M5x5

37	1	500511	HBS, M4x25

38	3	500512	HBS, M5x16

39	2	500513	HBS, M5x8

41	1	500514	Cam Group

42	1	430733	Assy

43	1	500516	Rear Bar Assy

44	1	500517	Press Bar Assy

45	1	500518	Front Bar Assy

46	1	500519	Transmission Group

51	1	500520	HBS,M5

52	2	500521	PMS, M3x20

53	3	500522	Micro Switch

54	2	500523	PW, M3

55	4	500524	SW, M3

56	2	500525	HN, M3

57	2	500526	PW, M4

58	2	500527	SW, M4

59	2	500528	PMS, M4x12

60	1	500529	Snap Ring E3

16

12/14/10

17

12/14/10

18

12/14/10

19

12/14/10

REAR BAR ASSEMBLY

| KEY 1 | QTY 1 | PART NO. 500575 | DESCRIPTION Spring Pin, 3x18 |
| --- | --- | --- | --- |
| 2 | 1 | 500576 | Return Spring |
| 3 | 1 | 500577 | Spring Hook |
| 4 | 1 | 500578 | Rear Bar |
| 5 | 1 | 430129 | Plunger |
| 6 | 1 | 500579 | Bearing, 635ZZ |
| 7 | 1 | 500580 | Spring Pin, 5x14 |
| 8 | 1 | 500581 | Spring |

20

12/14/10

PRESS BAR ASSEMBLY

| KEY 1 | QTY 1 | PART NO. 500584 | DESCRIPTION Press Bar |
| --- | --- | --- | --- |
| 2 | 1 | 500575 | Spring Pin, 3x18 |
| 3 | 1 | 500576 | Return Spring |
| 4 | 1 | 500577 | Spring Hook |
| 5 | 1 | 430129 | Plunger |
| 6 | 1 | 500579 | Bearing, 635ZZ |
| 7 | 1 | 500580 | Spring Pin, 5x14 |
| 8 | 1 | 500581 | Spring |

21

12/14/10

FRONT BAR ASSEMBLY

| KEY 1 | QTY 1 | PART NO. 500575 | DESCRIPTION Spring Pin, 3x18 |
| --- | --- | --- | --- |
| 2 | 1 | 500576 | Return Spring |
| 3 | 1 | 500577 | Spring Hook |
| 4 | 1 | 430129 | Plunger |
| 5 | 1 | 500579 | Bearing, 635ZZ |
| 6 | 1 | 500580 | Spring Pin, 5x14 |
| 7 | 1 | 500581 | Spring |
| 8 | 1 | 500587 | Front Bar |

22

12/14/10

23

12/14/10

MAIN ROLLER ASSEMBLY

| KEY 1 | QTY 1 | PART NO. 500599 | DESCRIPTION Main Roller Shaft |
| --- | --- | --- | --- |
| 2 | 1 | 500600 | Main Roller |
| 3 | 2 | 500601 | Side Plate |
| 4 | 1 | 500602 | Bearing, 6004ZZ |
| 5 | 1 | 500603 | Stop Ring, S-20 |
| 6 | 1 | 500604 | Gear |
| 7 | 1 | 500605 | Washer |
| 8 | 1 | 500508 | SW, M6 |
| 9 | 1 | 500495 | HBS, M6x16 |
| 10 | 1 | 500496 | HBS, M5x12 |
| 11 | 1 | 500606 | Key 5x5x35 |

24

12/14/10

FEED SHOOTER ASSEMBLY

| KEY 1 | QTY 1 | PART NO. 500628 | DESCRIPTION Feed Shooter |
| --- | --- | --- | --- |
| 2 | 2 | 500500 | SW,M5 |
| 3 | 2 | 500512 | HBS, M5x16 |
| 4 | 2 | 500629 | Ring, S10 |
| 5 | 1 | 500630 | Shaft |
| 6 | 1 | 500631 | Roller |
| 7 | 4 | 500632 | PW,M6 |
| 8 | 2 | 500508 | SW,M6 |
| 9 | 2 | 500495 | HBS, M6x16 |
| 10 | 2 | 500633 | HN,M6 |

25

12/14/10

ROLLER ARM ASSEMBLY

KEY	QTY	PART NO.	DESCRIPTION

| 1 | 1 | 500607 | Tension Arm |
| --- | --- | --- | --- |
| 2 | 1 | 500508 | Shaft |
| 3 | 1 | 500609 | Connect Rod |
| 4 | 1 | 500610 | Roller Arm |
| 5 | 1 | 500611 | Shaft |
| 6 | 1 | 500612 | Spring |
| 7 | 1 | 500613 | Roller Shaft |
| 8 | 1 | 500614 | Roller |
| 9 | 1 | 430705 | Feed Spring |
| 10 | 1 | 500616 | Washer |
| 11 | 1 | 500617 | Nut |
| 13 | 1 | 500619 | HBS, M6x75 |
| 14 | 1 | 500620 | HN, M6 |
| 15 | 2 | 500495 | HBS, M6x16 |
| 16 | 3 | 500508 | SW, M6 |
| 17 | 2 | 500621 | Bearing, 6001ZZ |
| 18 | 1 | 500622 | Snap Ring S12 |
| 19 | 1 | 500505 | HSS, M5x5 |
| 20 | 1 | 500623 | HBS, M5x40 |
| 21 | 1 | 500624 | Bearing, 635ZZ |
| 22 | 3 | 500499 | PW, M5 |
| 23 | 4 | 500563 | HN, M5 |
| 24 | 2 | 500500 | SW, M5 |
| 25 | 2 | 500625 | Snap Ring E6 |
| 26 | 2 | 500626 | Bushing |
| 27 | 1 | 500627 | HBS, M5x30 |
| 28 | 1 | 430718 | Spacer |
| 31 | 1 | 430719 | PW, M6 (C) |

26

12/14/10

27

12/14/10

28

12/14/10

29

12/14/10

30

12/14/10

BASE ASSEMBLY

| KEY 1 | QTY 1 | PART NO. 500652 | DESCRIPTION Frame |
| --- | --- | --- | --- |
| 1 | 1 | 500652 | Frame |
| 4 | 1 | 500656 | Support |
| 5 | 1 | 500657 | Side cover |
| 7 | 1 | 500658 | Hinge |
| 8 | 1 | 500659 | Grommet |
| 9 | 1 | 500660 | Front Door |
| 11 | 1 | 500662 | Grommet |
| 12 | 4 | 500663 | Fix Plate |
| 13 | 4 | 430706 | Adjustable Leg |
| 14 | 2 | 500665 | Caster (Free) |
| 15 | 2 | 500666 | Caster (Brake) |
| 16 | 2 | 500667 | Magnet Catch |
| 20 | 14 | 500508 | SW, M6 |
| 21 | 10 | 500649 | PW, M6 |
| 24 | 3 | 500633 | HN, M6 |
| 25 | 4 | 500496 | HBS, M5x12 |
| 28 | 1 | 500668 | Collar |
| 29 | 1 | 500669 | FMS, M6x8 |
| 30 | 2 | 500670 | FMS, M4x8 |
| 31 | 4 | 500527 | SW, M4 |
| 32 | 2 | 500503 | HN, M4 |
| 33 | 4 | 500671 | TMS, M4x8 |
| 34 | 4 | 500672 | TMS, M3x8 |
| 35 | 1 | 430726 | HBS, M6x35 |
| 37 | 2 | 500674 | Collar |
| 38 | 8 | 500500 | SW, M5 |
| 39 | 1 | 500675 | HBS, M4x8 |
| 40 | 1 | 500676 | Grommet |
| 41 | 8 | 500495 | HBS, M6x16 |
| 47 | 1 | 500682 | Grommet |
| 51 | 8 | 500499 | PW, M5 |
| 56 | 2 | 500683 | Top Plate Holder |
| 57 | 4 | 500684 | HBS, M6x12 |
| 58 | 4 | 430724 | SW, M16 |
| 61 | 2 | 430725 | Cushion |
| 62 | 1 | 430484 | Heater Transformer Ass’y (110V) |
| 63 | 1 | 430518 | Terminal Bracket |
| 64 | 4 | 430340 | TMS, M4×6 |
| 65 | 2 | 430100 | PMS, M4×8 |

31

12/14/10

32

12/14/10

TOP PLATE ASSEMBLY

| KEY 1 | QTY 1 | PART NO. 500685 | DESCRIPTION Top Plate |
| --- | --- | --- | --- |
| 2 | 1 | 500686 | Package Guide |
| 3 | 2 | 500687 | Shaft |
| 4 | 2 | 500688 | HBS M6x12 |
| 5 | 2 | 500508 | SW,M6 |
| 6 | 4 | 500649 | PW,M6 |
| 7 | 2 | 500689 | WN, M6 |
| 8 | 1 | 500690 | TMS, M6x8 |
| 9 | 2 | 500691 | TMS, M5x8 |
| 10 | 1 | 500692 | Top Plate (OPTION For with Readout) |
| 11 | 1 | 500693 | Grommet (OPTION For with Readout) |

33

12/14/10

34

12/14/10

REEL CONTROL ASSEMBLY

| KEY 1 | QTY 1 | PART NO. 500696 | DESCRIPTION Reel Shaft |
| --- | --- | --- | --- |
| 2 | 1 | 500697 | Lid |
| 3 | 1 | 500698 | Brake Shaft |
| 4 | 2 | 500699 | Bearing |
| 5 | 1 | 500700 | Washer |
| 6 | 1 | 500701 | Reel In Circular |
| 7 | 1 | 500702 | Reel Out Circular |
| 8 | 1 | 500703 | Protector |
| 9 | 1 | 500704 | Reel Nut Handle |
| 10 | 1 | 500705 | Brake Lining |
| 11 | 1 | 500706 | Roller |
| 12 | 1 | 500707 | Pin |
| 13 | 1 | 500708 | Split Pin |
| 14 | 1 | 500709 | Roller Holder |
| 15 | 1 | 500710 | Brake Adjuster |
| 16 | 1 | 500711 | Spring |
| 17 | 1 | 500712 | Reel Support |
| 18 | 1 | 500713 | Lining Fixed Bracket |
| 19 | 1 | 500714 | Arm |
| 20 | 1 | 500715 | Lining Holder |
| 21 | 3 | 500633 | HN, M6 |
| 22 | 2 | 500495 | HBS, M6x16 |
| 23 | 1 | 500716 | HBS M8x16 |
| 24 | 2 | 500717 | Stop Ring S-20 |
| 25 | 1 | 500718 | Stop Ring S-10 |
| 27 | 1 | 500720 | Center Drum 280MM |
| 28 | 1 | 500721 | Washer |
| 29 | 1 | 500722 | E Ring E19 |
| 30 | 1 | 500623 | HBS, M4x25 |
| 31 | 2 | 500724 | 14N, M4 |
| 32 | 3 | 500725 | PMS, M4x16 |
| 33 | 3 | 500526 | PW, M4 |
| 34 | 1 | 500508 | SW, M6 |
| 35 | 1 | 500726 | Stop Ring S-15 |
| 36 | 1 | 500727 | Holder |

35

12/14/10

36

12/14/10

ELECTRONIC CONTROL ASSEMBLY

| KEY 1 | QTY 1 | PART NO. 500696 | DESCRIPTION Reel Shaft |
| --- | --- | --- | --- |
| 1 | 1 | 500728 | Electric Control Unit |
| 2 | 1 | 500729 | Electric Control Unit w/ read out |
| 3 | 1 | 500730 | Indicator Unit (Option) |

37

12/14/10

ELECTRONIC CONTROL COMPONENTS

| KEY 1 | QTY 1 | PART NO. 500731 | DESCRIPTION Box |
| --- | --- | --- | --- |
| 1 | 1 | 500731 | Box |
| 2 | 1 | 500732 | Cover |
| 3 | 1 | 500733 | Transformer (110V) |
| 4 | 1 | 430727 | P.C.Board |
| 5 | 1 | 430728 | Panel |
| 6 | 3 | 500736 | Fuse Holder |
| 7 | 1 | 500737 | Fuse (115V/3A) |
| 8 | 1 | 500738 | Fuse (1A) |
| 9 | 1 | 500739 | Fuse (10A) |
| 10 | 1 | 500740 | Fuse (7A) |
| 11 | 11 | 500741 | Knob |
| 12 | 2 | 500742 | Knob |
| 13 | 4 | 500743 | Variable Resistor |
| 14 | 1 | 500744 | Grommet |
| 15 | 1 | 500745 | Power Switch |
| 16 | 1 | 500746 | Heater Lamp |
| 17 | 1 | 500747 | Knob |
| 18 | 1 | 500748 | Selector Switch (Feed/Reset) |
| 19 | 1 | 500749 | Knob |
| 20 | 1 | 500750 | Panel |
| 21 | 1 | 430715 | Earth Plate (5P) |
| 22 | 1 | 500751 | Power Cord |
| 23 | 4 | 500528 | PMS, M4x12 |
| 24 | 4 | 500527 | SW, M4 |
| 25 | 4 | 500503 | HN, M4 |
| 26 | 4 | 500752 | Bolt |
| 27 | 8 | 500524 | SW, M3 |
| 28 | 8 | 500525 | HN, M3 |
| 29 | 4 | 500753 | PMS, M6x10 |
| 30 | 6 | 500754 | PMS, M4x8 |
| 32 | 2 | 430716 | PW, M4 |
| 33 | 1 | 430717 | TMS, M4x12 |
| 40 | 1 | 430729 | P.C.B. For Machine With Readout (Optional) |
| 41 | 1 | 500888 | X1 Wire harness |
| 42 | 1 | 500887 | X2 Wire harness |
| 43 | 1 | 500886 | X3 Wire harness |
| 44 | 1 | 430730 | X4 Wire harness |
| 45 | 1 | 500884 | X5 Wire harness |
| 46 | 1 | 500883 | X6 Wire harness |
| 47 | 1 | 500882 | X7 Wire harness |
| 50 | 1 | 430731 | Label |
| 51 | 1 | 430732 | Label |

38

12/14/10

39

12/14/10

INDICATOR UNIT ASSEMBLY OPTION

| KEY 1 | QTY 1 | PART NO. 500755 | DESCRIPTION Tension And Length Indicators |
| --- | --- | --- | --- |
| 2 | 1 | 500756 | Indicators Under Cover |
| 3 | 1 | 500757 | Indicators Support |
| 4 | 1 | 500758 | Indicators Upper Cover |
| 5 | 4 | 500759 | PMS, M4x8 |
| 6 | 2 | 500760 | Screw |
| 7 | 1 | 500761 | Bolt |

40

12/14/10

SPARE PARTS KIT (P/N 500765)

| QTY 1 | PART NO. 500584 | DESCRIPTION Press Bar |
| --- | --- | --- |
| 2 | 500579 | Bearing, 635ZZ |
| 2 | 500522 | Micro Switch |
| 1 | 430189 | Heater |
| 2 | 500576 | Return Spring |
| 1 | 500600 | Main Roller |
| 1 | 500734 | P.C. Board |
| 2 | 500737 | Fuse, 3 AMP |
| 2 | 500738 | Fuse, 1 AMP |
| 2 | 500739 | Fuse, 10 AMP |
| 2 | 500740 | Fuse, 7 AMP |

41

12/14/10

DISTRIBUTOR SALES

www.signodedistributors.com

© Copyright 2006 Signode  500762  Rev. 12/2010

# Text boxes

16        1            430720            Stop

17        1            430721            Insert

18        2            430722            Screw

19        1            430723            Nut

| CONTENTS | Page |
| --- | --- |
| Safety Information | 3 |
| Specifications | 5 |
| Major Components | 6 |
| Disconnect & Lockout | 8 |
| Electrical Schematic | 9 |
| Operation | 13 |
| Parts List & Views | 15 |
| Spare Parts | 41 |

| PARTS LISTS & EXPLODED VIEW |
| --- |
| INTERNAL GROUPS: | Page |
| Control Head | 16 |
| Cam | 18 |
| Heater | 19 |
| Rear Bar | 20 |
| Press Bar | 21 |
| Front Bar | 22 |
| Feed | 23 |
| Main Roller | 24 |
| Feed Shooter | 25 |
| Roller Arm | 26 |
| Strap Guide | 28 |
| Transmission | 29 |
| EXTERNAL: |  |
| Frame | 30 |
| Base | 31 |
| Top Plate | 33 |
| Reel Unit | 34 |
| Reel Control | 35 |
| ELECTRICAL: |  |
| Control Unit | 37 |
| Control Components | 38 |
| OPTIONS: |  |
| Indicator Unit | 40 |
| SPARE PARTS LIST | 41 |